SOPRANATURE SPECIFICATION
TOUNDRA BOX - MODULAR SYSTEM           CONVENTIONAL ROOFING    ASSEMBLY

THESE MASTER SPECIFICATIONS CONTAIN ALL SPECIFICATIONS FOR EACH SPECIFIC SOPREMA ROOFING MEMBRANE SYSTEM

THE EDITOR SHOULD CONTACT A SOPREMA REPRESENTATIVE TO GET ASSISTANCE FOR THE ADAPTATION OR COMPLETION OF SPECIFICATIONS ACCORDING TO THE PARTICULAR CONDITIONS RELATED TO EACH PROJECT.

IMPORTANT: STRUCTURAL LOAD CAPACITY MUST BE CONSIDERED BEFORE CHOOSING AND SPECIFYING EACH PARTICULAR SYSTEM. THE STRUCTURE’S ABILITY TO SUPPORT THE ADDITIONAL WEIGHT OF A SOPRANATURE SYSTEM MUST FIRST BE EVALUATED AND APPROVED BY A PROFESSIONAL ENGINEER.

A SOURCE OF WATER MUST BE AVAILABLE ON THE ROOF THROUGHOUT THE INSTALLATION AND THEREAFTER AVAILABLE PERMANENTLY.

IMPORTANT: PLEASE BE SURE TO READ THE POLICY STATEMENT IN THE IMPORTANT NOTICES SECTION IN THE FIRST PAGES OF THE SOPREMA ROOFING SYSTEMS BINDER.

FOR A COMPLETE DESCRIPTION OF PRODUCTS AND APPLICABLE STANDARDS, PLEASE REFER TO THE TECHNICAL DATA SHEETS ON OUR WEBSITE AT WWW.SOPREMA.CA.

# General

## REFERENCE STANDARD[S]

NOTE TO THE SPECIFIER: The designer of the waterproofing system should investigate with the client which requirements apply to a particular project. Applicable building regulations must be followed. Consult provincial roofing associations, since they could have special requirements, particularly if they offer warranties.

NOTE TO THE SPECIFIER: The National Building Code requires that all roofs, except when permitted (tents, inflatable structures, certain small “assembly occupancy” buildings), must be Class A, B, or C, as determined in accordance with CAN/ULC-S107-10 “Standard Methods of Fire Tests of Roof Coverings.”

#### [Submit a report, issued by a certified materials testing laboratory, attesting that the specified roofing system was tested in accordance with CSA A123.21-14, Standard test method for the dynamic wind uplift resistance of membrane-roofing systems. Test results shall demonstrate that the roofing system provides a Dynamic Uplift Resistance (DUR) of [   ] kPa for the field surface of the roof, [   ] kPa for the edges of the roof, and [   ] kPa for the corners of the roof.]

#### [Submit a report, issued by a certified materials testing laboratory, attesting that the specified modular system was tested in accordance with CSA A123.24-15, Standard test method for wind resistance of modular vegetated roof assembly.]

#### [Roofing system must meet or exceed requirements of CAN/ULC-S107-10, Methods of Fire Tests of Roof Coverings, Class [A] [B] [C].]

#### Root barrier must meet requirements of ANSI/GRHC/SPRI VR-1 2011, Procedure for Investigating Resistance to Root Penetration on Vegetative Roofs.

#### [Ballast must meet or exceed requirements of ASTM D7655-12, Standard Classification for Size of Aggregate Used as Ballast for Membrane Roof Systems.]

#### [Ballast must meet or exceed requirements of ASTM D1863-05, Standard Specification for Mineral Aggregate Used on Built-Ups Roofs.]

## COMPATIBILITY

#### Except vegetation, all the materials specified in this document must be provided by the same manufacturer.

## TECHNICAL DOCUMENTS

#### Submit two (2) copies of the most current technical data sheets. These documents must describe the physical properties of materials [and explanations about product installation, including restrictions, limitations and other manufacturer recommendations].

## QUALITY ASSURANCE AND ENVIRONMENTAL MANAGEMENT

NOTE TO THE SPECIFIER: Certificates of qualification may be part of the documents required for submission. Where applicable, these requirements shall be part of the call for tender(s).

#### The manufacturer of elastomeric bitumen products will provide proof of ISO 9001 and ISO 14001 Certifications.

## CONTRACTOR QUALIFICATIONS

#### The contracted installer and his subcontractors must be officially recognized as authorized contractors by the vegetated roofing system supplier at the time of tendering and throughout installation.

#### Required work may be carried out only by applicators who have been trained in the application of the green roofing systems and who are employed by an enterprise which has the adequate and necessary equipment.

## MANUFACTURER’S REPRESENTATIVE

#### A representative of the waterproofing materials manufacturer can be present on the worksite at commencement of work or at any other time during the work, as required.

#### The contractor must at all times enable and facilitate access to the worksite and the roofs for the said manufacturer’s representative.

## MATERIAL STORAGE

#### Delivered materials will be carefully housed and, if required, adequately protected in a dry, ventilated shelter, protected from frost and the elements, as well as all harmful substances.

#### Installation needs to take place within the first 48 hours after delivery. If it is not possible, plants must be stored outdoors and unstacked in their original containers and watered every day.

#### Avoid the accumulation of materials on the roofs, which could, in specific areas, compromise structural soundness by placing more weight on it than is recommended.

## WARRANTIES

NOTE TO THE SPECIFIER: Please refer to the National Master Specifications (NMS) for federal government contracts. For other works, please refer to the following term(s). For more information on roofing membrane warranty, please consult SOPREMA's warranties (of which terms must in no way be modified).

NOTE TO THE SPECIFIER: Retain the following article when a green roofing material warranty (SOPRANATURE) is requested in addition to a SOPREMA MAMMOUTH PLATINUM SBS system warranties or GENERATION warranty (warranty of the membrane manufacturer).

#### The membrane manufacturer will issue a written document in the owner’s name, valid for a [   ]-year period, stating that it will provide the necessary labour and Products for the removal and reinstallation of the SOPREMA SOPRANATURE Products to restore the roofing system to a dry and watertight condition. The warranty must cover the total cost of repair(s) during the entire warranty period. About the maintenance of the plants, the owner will be fully responsible. The warranty must be transferable, at no extra cost, to subsequent building owners. The warranty certificate must reflect these requirements.

# Products

## ROOT BARRIER

#### Description: Woven high density polyethylene scrim of [0.5 mm (20 mil)] [0.76 mm (30 mil)] thick that offers protection against migration of roots.

#### Specified product: SOPRABARRIER [20] [30] by SOPREMA

## ROOT BARRIER SEALING TAPE

#### Description: Polyethylene film, single coated with a rubber pressure sensitive adhesive designed for sealing root barrier longitudinal and transversal laps.

#### Specified product: [SOPREMA APPROVED TAPE] [   ]

## ACCESSORIES

### Protective borders

NOTE TO THE SPECIFIER: Gravel or paver protection must be laid over the area within 300 mm of the edge. This area must be isolated from the SOPRANATURE system by curbs made of L shaped aluminum, zinc or galvanized steel, or with a concrete, interlocking paving stone or treated wood-rafter border.  These curbs will be installed on the drainage panels. Contact a SOPRANATURE representative to propose a layout plan using these elements.

NOTE TO THE SPECIFIER: If the metal edges are not slotted, drainage must be installed under those edges to allow water circulation.

#### Description: [Slotted] L-shaped 16 ga (0.051”) aluminum angle designed to retain the components of the vegetated roof systems and delimit vegetation-free borders.

#### Dimensions: [100 x 100 mm (4 x 4 in)] [125 x 125 mm (5 x 5 in)] [150 x 150 mm (6 x 6 in)] [200 x 200 mm (8 x 8 in)]

#### Specified Product: SOPRANATURE METAL EDGING

### Paver pedestals

#### Description: Polypropylene support for pavers used for pedestrian traffic terraces. The pedestals consist of an adjustable screw nut head assembly and a base. [The slope corrector may be installed at the base to level slopes of 0 to 5%.] [The 2 mm (80 mil) foam cushion is used to absorb shocks and to prevent pavers from moving.]

#### Properties:

##### Ultimate strength: (1 ton loaded on whole surface > 500 kg (1,102 lb) loaded on one fourth of the surface.

##### Height: [35 mm (1,37 in)] [40-67 mm (1,58-2,64 in)] [60-90 mm (2,36-3,54 in)] [90-150 mm (3,54-5,90 in)] [150-260 mm (5,90-10,23 in)]

#### Specified product: PAVER PEDESTAL by SOPREMA.

## MODULAR SYSTEM

#### Description: Pre-vegetated system composed of a box made of 100% recycled polypropylene and recyclable removable side boards, containing a filter cloth and a growing medium in which a mix of sedum species is cultivated.

#### Specified product: TOUNDRA BOX by SOPREMA

## FERTILIZERS, CONDITIONERS AND ADDITIVES

#### Specified Product: [   ]

## BALLAST FOR VEGETATION-FREE BORDERS

### River Gravel

#### Description: Gravel shall be round, washed, and exempt of dust, humidity, ice, snow and foreign objects. Nominal diameter is 38 mm (1.5 in).

### Pavers

#### Description: Prefabricated concrete pavers [of [     ] mm x [     ] mm x [     ] mm  ([     ] in x [     ] in x [     ] in) in thickness].

# Execution of Work

## SURFACE EXAMINATION AND PREPARATION

#### Surface examination and preparation must be completed in conformance with instructions in the membrane manufacturer’s technical documentation.

#### Before landscaping work begins, the owner's representative and foreman of the roofing contractor will inspect and approve waterproofing membranes conditions as well as flashings at parapets, roof drains, plumbing vents, ventilation outlets and other construction joints. If necessary, a non-conformity notice will be issued to the contractor so that required corrections can be carried out. The start of landscaping work will be considered as acceptance of conditions for work completion.

## METHOD OF EXECUTION

#### Ballast the light components that are likely to move around or fly away due to wind gusts.

## INSTALLATION OF ROOT BARRIER

#### Unroll the root barrier over the entire surface, directly onto the waterproofing membranes, overlapping the joints by 305 mm (12 in). Seal the joints with the seaming tape. Apply up the parapet walls and other upstands to the top level of the vegetation-free zone.

## INSTALLATION OF ACCESSORIES AND BALLAST

#### Install protective borders, paver pedestals and ballast directly onto the root-barrier at required locations.

## INSTALLATION OF MODULAR SYSTEM

NOTE TO THE SPECIFIER: SOPRANATURE Modular System contains all the required components to allow plants to grow and flourish. The module allows for water retention and drainage of the excess of water.

#### Lay the modules directly on the root barrier, aligned, side by side.

#### Remove the side boards of the second to last row.

#### Recycle side boards.

#### Use angle grinder or reciprocating saw if trimming is required.

#### Water the modules to saturation.

## MAINTENANCE OF GREEN ROOFING SYSTEMS

IMPORTANT: Ensure the owner is made aware of the following maintenance recommendations. Maintenance must be carried out in conformance with these directives. The green roof’s success depends in large part on following these recommendations. Maintenance can be carried out by the building owner or by the installation professional. Refer to the Sopranature Maintenance Guide on the SOPREMA website for more details.

NOTE TO THE SPECIFIER: A water source (tap) must be installed before the beginning of work and must always be accessible close to all green roofs.

#### Irrigation is necessary depending on the climate and the plants’ requirements. It can be accomplished naturally (rain), manually (hose and/or watering can and/or sprinkler) or with an automatic irrigation system (drop by drop irrigation and/or sprinklers).

#### Maintenance of a green roofing system requires a variety of measures after vegetation is installed to ensure its durability. These operations include fertilization, weeding, pruning, mowing or harvesting, as well as collection of cuttings.

#### Four visits minimum are recommended each year for the maintenance of green roofs. The frequency of maintenance (weeding) can be higher during the first two years to ensure the dominance of the desired vegetation cover.

#### Fertilization of extensive green roof systems includes the light application of a slow-release organic or chemical fertilizer every two or three years. It is recommended to fertilize water and trim extensive systems to a minimal extent, in order to stimulate establishment and foster resistance to drought and cold.

#### The growing medium must be watered to saturation before any application of soluble fertilizer to avoid burns and the leaching of nutrients to the roof drains.

#### Inspect and clean drains during every maintenance period.

Based on the evolution of knowledge and techniques, SOPREMA INC. may modify the composition and/or conditions of use of its products without prior notice. Consequently, orders will be filled according to the latest specifications.

- END OF SECTION -